## Slide 1: Automated Fish Species Classification Using Sonar and Machine Learning
Shiheng Huang

## Slide 2: Background
Ontario Government needs to perform ecological monitoring in Ontario lakes
  To know what’s in the lake
  Approximate fish population
  Provide guidance for the inland fisheries
Picture sources from Toronto and Region Conservation Authority

## Slide 3: Existing Methods
Trawling / Netting
- Towing a large, cone-shaped net (a trawl) through the water to catch fish
- Invasive and harm fish population
- Time consuming and expensive
- Limit large-scale or frequent monitoring
Hydroacoustic
- Uses sonar technology to track and assess fish populations and their behavior by analyzing sound waves reflected off fish
- Non-invasive
- Rely on manual interpretation

## Slide 4: Research Questions
Developed automated workflow to implement hydroacoustic with Machine Learning techniques
  Build Machine Learning models to automatically classify fish species using labeled data
  Focus on fish-level classification at the moment

## Slide 5: Data - RAW
FishNum | species | totalLength | ... | pingNumber | F45 | ... | ... | F260
LT001 | lakeTrout |  |  | 1 |  |  |  | 
LT001 | lakeTrout |  |  | 2 |  |  |  | 
LT001 | lakeTrout |  |  | 3 |  |  |  | 
... | ... |  |  | ... |  |  |  | 
SMB013 | smallmouthBass |  |  |  |  |  |  | 
Fish Characteristics
Target Strength
14574 observations, 484 variables
21 Lake Trout, 11 Lake Whitefish, 12 Smallmouth Bass

## Slide 6: Data - Processed
14392 observations, 264 variables
21 Lake Trout, 10 Lake Whitefish, 12 Smallmouth Bass
FishNum | species | F45 | ... | F89.5 | F173 | ... | ... | F260
LT001 | lakeTrout |  |  |  |  |  |  | 
LT001 | lakeTrout |  |  |  |  |  |  | 
LT001 | lakeTrout |  |  |  |  |  |  | 
... | ... |  |  |  |  |  |  | 
SMB013 | smallmouthBass |  |  |  |  |  |  | 

## Slide 7: Data Exploration

## Slide 8: Proposed Methods
Multinomial Regression
Simple baseline model to test linear relationship in the data
Provide interpretable results and computationally lightweight
Random Forest
Handle hierarchical structure of high-dimensional fish signatures
Robust to noise and overfitting, reveal feature importance
Deep Neural Network
Learn complex, non-linear hierarchical interactions
Automatic layered abstraction
LSTM (Long Short-Term Memory)
Designed for sequential data
Incorporate fish habitat context for temporal patterns
Notes: Multinomial Regression
  Simple baseline model to test linear relationship in the data
  Provide interpretable results and computationally lightweight
Random Forest
  Handle hierarchical structure of high-dimensional fish signatures
  Robust to noise and overfitting, reveal feature importance
Deep Neural Network
  Learn complex, non-linear hierarchical interactions
  High accuracy with
LSTM (Long Short-Term Memory)
  Designed for sequential data
  Incorporate fish habitat context for temporal patterns

## Slide 9: Proposed Methods – Input Data
Multinomial Regression
Mean TS for each fish
Standardized and apply PCA (first two PCs)
Dim: 43 x 267
Random Forest
Raw data
Dim: 14392 x 267
Deep Neural Network
Raw data
Dim: 14392 x 267
LSTM
Standardized 3D array
Dim: 43 x 1619 (N) x 267
Frequency response (Dim 3)
Fish ID (Dim 1)
Ping1
Ping2
Ping3
SMB013
LWT001
LT001
Ping sequence (Dim 2)
Notes: Multinomial Regression
  Simple baseline model to test linear relationship in the data
  Provide interpretable results and computationally lightweight
Random Forest
  Handle hierarchical structure of high-dimensional fish signatures
  Robust to noise and overfitting, reveal feature importance
Deep Neural Network
  Learn complex, non-linear hierarchical interactions
  High accuracy with
LSTM (Long Short-Term Memory)
  Designed for sequential data
  Incorporate fish habitat context for temporal patterns

## Slide 10: Results
Multinomial Regression
Accuracy: 37.5%
Apply PCA and uses first two PCs (Cum Var: 95.9%)
Random Forest
Accuracy: 62.5%
Mtry: 20, n_Trees: 400, min_n: 5
Deep Neural Network
Accuracy: 62.5%
3 hidden layer, epochs: 128
LSTM
Accuracy: 62.5%
2 LSTM layers, 1 hidden layer, epochs: 21
Actual Predicted | LT | LWT | SMB
LT | 3 | 1 | 2
LWT | 0 | 0 | 0
SMB | 1 | 1 | 0
Actual Predicted | LT | LWT | SMB
LT | 4 | 1 | 2
LWT | 0 | 1 | 0
SMB | 0 | 0 | 0
Actual Predicted | LT | LWT | SMB
LT | 4 | 1 | 2
LWT | 0 | 1 | 0
SMB | 0 | 0 | 0
Actual Predicted | LT | LWT | SMB
LT | 2 | 0 | 1
LWT | 1 | 2 | 0
SMB | 1 | 0 | 1
Notes: Multinomial Regression
  Simple baseline model to test linear relationship in the data
  Provide interpretable results and computationally lightweight
Random Forest
  Handle hierarchical structure of high-dimensional fish signatures
  Robust to noise and overfitting, reveal feature importance
Deep Neural Network
  Learn complex, non-linear hierarchical interactions
  High accuracy with
LSTM (Long Short-Term Memory)
  Designed for sequential data
  Incorporate fish habitat context for temporal patterns

## Slide 11: Future STEPs
Enhanced LSTM with attention mechanism
  Focus on most informative signal
  Less focus on the less important signal
Incorporate Fish characteristics
  Signal variation within species might relate to weight, total length, gender, etc.
More details can be view at GitHub: Fish Classification

## Slide 12: Thank you